## Slide 1: Hardware and Features of various Storage Technologies

## Slide 2: Agenda
Overview of DAS, NAS, and SANs

## Slide 3: What is DAS?
Advantages: Disadvantages:
Easy to configure (hard drives connecting directly to a computer through a HBA.
Inexpensive solution
Isolated, because the disks are attached to a single server
Less flexible for allocation additional storage.
DAS is physically attached to the server. comes in various disk types, such as Serial ATA (SATA), serial attached SCSI (SAS), or solid-state drive (SSD).
Server with attached disks
Notes: Explain that DAS is the most common storage system that is available today, and ensure that students know that DAS is easy to install and configure. However, you should explain that it could be complex to manage a large deployment of servers that all are using DAS, because data is in many different locations.
Mention that servers can use DAS along with other storage types and that in many cases, servers use DAS for the system drives that start up the computer, and then use a NAS device or SAN storage to store data.
20740C
3: Implementing enterprise storage solutions

## Slide 4: What is NAS? (try FreeNAS)
NAS differs from DAS because the storage does not attach directly to each individual server, but rather is accessible across a network to many servers. NAS has two distinct solutions:
A low-end appliance (NAS only)
An enterprise class NAS that integrates with a SAN.
Each NAS device has a dedicated operating system that solely controls data access on that device, which reduces the overhead associated with sharing the storage device with other server services. Windows Storage Server, a feature of Windows Server 2016, is an example of NAS software.
NAS devices provide file-level access to storage, which means that data in the storage is accessible only as files and folders, and you must use protocols such as Common Internet File System (CIFS), Server Message Block (SMB), or network file system (NFS) to access the files.
NAS is storage that is attached to a dedicated storage device and accessed through network shares
Notes: One key point to make is that you typically operate NAS by using software, and therefore, it can have some latency issues. A NAS device can be a computer that is running Windows Storage Server or some sort of clustering software, but essentially, it is a file server with no other role capabilities.
20740C
3: Implementing enterprise storage solutions

## Slide 5: What is NAS?
Advantages:
Simple, relatively inexpensive, fits nicely into the market as a mid-priced solution.
NAS typically includes Redundant Array of Independent Disks (RAID) for data redundancy
NAS offers centralized storage at an affordable price
A Plug and Play (PNP) solution that is easy to install, deploy, and manage.
NAS units are accessible from any operating system. They often have multiple-protocol support and can serve up data via CIFS and NFS simultaneously
Disadvantages:
Slower access times than SAN technologies. You typically access NAS by using Ethernet protocols, and it relies heavily on the network. Therefore, NAS commonly is used as a file sharing/storage solution, but you cannot (and should not try to) use it with data-intensive programs such as Microsoft Exchange Server and Microsoft SQL Server.
Not an enterprise solution
File server
Local Area
Network
(Ethernet)
NAS device
File-level access
(CIFS, NFS)
Network
Notes: One key point to make is that you typically operate NAS by using software, and therefore, it can have some latency issues. A NAS device can be a computer that is running Windows Storage Server or some sort of clustering software, but essentially, it is a file server with no other role capabilities.
20740C
3: Implementing enterprise storage solutions

## Slide 6: What is a SAN?
Advantages:
Fastest access times
Easily expandable
Centralized storage
High level of redundancy
Disadvantages:
More expensive
Requires specialized skills
SANs offers higher availability with the most flexibility
Implement SANs by using Fibre Channel or iSCSI
Servers
Switches
Storage devices
Notes: Explain that SAN provides the most flexibility, in comparison to other storage types such as NAS. However, further explain that it is the most expensive to implement, and typically requires specialist skills to operate and manage.
Use the slide’s diagram to illustrate how you implement a SAN. Start by showing a simple SAN deployment with one or two servers, and a single network switch and storage device. You then can expand the complexity and describe how you can increase redundancy, performance, and capacity by adding more network connections and paths, and by adding more storage devices.
20740C
3: Implementing enterprise storage solutions